|  | 719. ENERGY CONSERVATION GUIDELINES |
| --- | --- |
|  | It is essential that these energy guidelines be observed in the operation of cooling/heating equipment and general energy usage. The teacher will be responsible for implementing the guidelines during the time that s/he is present in the classroom. The principal will be responsible for total energy usage of his/her building. The principal will be provided information by the Director of Buildings & Grounds reflecting the energy consumption on a monthly basis for his/her building. The Director of Buildings & Grounds will provide support for each building energy conservation effort. A. GOALS FOR DISTRICT ENERGY PROGRAM 1. Conserve energy so that the instructional program and support services can be effectively delivered while conserving energy dollars. 2. Eliminate energy waste in our buildings and at the same time ensure a comfortable and safe learning environment for all students and staff. 3. Educate every student and employee to contribute to energy efficiency in our District. Every person will be expected to be an “energy saver” as well as an “energy consumer”. B. PROCEDURES FOR GENERAL ENERGY USAGE 1. Maintain an environment that is conducive to the educational process, the classroom temperature should be in the following range: a. Between 72 and 76 degrees during the cooling season b. Between 68 and 72 degrees during the heating season NOTE: If temperatures are outside of these ranges, report it to the building custodian. 2. Areas that are not occupied (even it left for a short period of time) will have lighting turned off. After the school day, custodians will turn on lighting only in areas they are working on for scheduled facility use. 3. Lights in all gymnasiums, cafeterias and auditoriums should not be left on unless the area is being utilized. 4. All outside lights should be turned off during daylight hours. 5. The exhaust fans in the rest rooms shall be turned off during periods of time the buildings are not occupied. 6. The office staff should turn off copy machines, laminating equipment, and other office machines each night. 7. All classroom computers should be turned off during periods of time the buildings are not occupied. Computer labs should be turned off over weekends and vacation periods. 8. Space heaters (use 1000 watts per hour) are to be eliminated from use in all buildings. Flat leg or foot warmers can be substituted and use much less energy (approximately 100 watts per hour). These devices must be turned off at the end of the day. 9. Personal electrical appliances: Refrigerators (compact) are permitted in the classroom only for curricular use. Coffee pots are permitted in selected rooms to brew coffee. Coffee would then be emptied into a thermos type device and the warmers turned off. Microwaves, toaster ovens and hot plates are not permitted in the classrooms. 10. The custodian at each school will be responsible for operating the building in an unoccupied mode at the closing of each school day or scheduled facility use. 11. Any area showing signs of mold should be reported to the day custodian. C. PROCEDURES FOR OPERATING HEATING EQUIPMENT 1. The thermostat controls shall be set no higher than 72 degrees; the Director of Buildings & Grounds must approve exceptions in advance. 2. Individual classroom and office doors will be closed when the heating equipment is in operation. 3. In the buildings with automatic temperature controls, the start time for the heating equipment should be set as late as possible while allowing time to heat the building to guideline temperature by the beginning of class. 4. In those buildings with automatic temperature controls, the thermostat will be set at 55 degrees at the close of the school day or scheduled facility use. 5. The principal will ensure that the custodians perform an end-of-day shutdown checklist on Monday through Thursday and a weekend shutdown checklist on Friday to make certain that the building systems are shut down in an energy conservative manner. 6. All domestic hot water systems are to be set no higher than 120°F or 140°F for cafeteria service (with dishwasher booster). Ensure all domestic hot water recirculating pumps are off during unoccupied times. 7. During spring and fall when there is no threat of freezing, all steam and forced air heating systems should be switched off during unoccupied times. Hot water systems should be switched off using the appropriate loop pumps. 8. If, on extremely cold nights, a 55 degree setback could cause coil freeze ups or not allow the building to heat to a comfortable level by the time students arrive, take the following action: a. Set the unoccupied temperature setting at 60 degrees. b. Contact the Director of Buildings & Grounds immediately. D. PROCEDURES FOR OPERATING AIR CONDITIONING EQUIPMENT 1. When the temperature is such that cooling is needed at the beginning of the school day, the start time for air conditioning equipment should be set as late as possible while still allowing time to cool the building to guideline temperature settings. 2. Set the thermostat controls in the range of 72 to 76 degrees when air conditioning is in operation. 3. Refrain from turning lights on unless definitely needed. Remember that lights not only consume electricity, but also give off heat, which in turn, places an additional load on the air conditioning equipment and thereby increases the use of electricity necessary to cool the room. 4. The air conditioning equipment should be turned off at the approximate time the students leave school. It is anticipated that the temperature of the classroom will be maintained long enough to afford comfort for the period the teacher remains in the classroom after the students have left. 5. Under no circumstances will air conditioning be utilized in classrooms during the summer months unless the classrooms are occupied. The Director of Buildings & Grounds must approve exceptions. 6. Where cross-ventilation is available during periods of mild weather, shut down air conditioning equipment and adjust the temperature by opening windows and doors. 7. Close individual classroom, office doors, and windows when the air conditioning equipment is in operation. 8. In situations where the air conditioning is running in unoccupied areas (ex. Floor wax will not dry due to high humidity, indoor air problems, etc.) outside make up air-dampers will be placed in the fully closed position. These situations must have prior approval of the Director of Buildings & Grounds. 9. Ensure that air conditioning systems operated from automatic temperature controls have outside air-dampers closed during unoccupied times. 10. For any 24-hour period the targeted relative humidity should not average greater than 60%. E. PROCEDURES FOR WATER CONSERVATION 1. Ensure that all plumbing (leaks, faucets, flush valves, etc.) and/or areas where water is entering the building (i.e., roof leaks, basement water intrusions) or humidity sources (condensation on pipes, sweating walls) are reported and repaired immediately. 2. All watering should be done between 5:00 A.M. and 10:00 A.M. |